## Slide 1: Technical Analysis of Early PCs and DOS
Rorabaugh, Tyler L.

## Slide 2: Overview
Analysis of the PC:
  Hardware
Analysis of DOS:
  Software
Impacts on Modern Technology:
  Operating Systems
  Computer Hardware

## Slide 3: The PC:
IBM PC, Low Cost
  PC – 1981
  XT – 1983
  AT – 1984
Compatible Clones
  Helped establish popularity
Open Standards, Popularity:
  Third Party Devices
  Third Party Software

## Slide 4: PC Hardware: Processors
8088
  Same as 8086 but 8 bit data bus
  Used in IBM PC and XT
  8087 optional FPU
80286
  Used in IBM AT
  Faster, memory management, more memory
  Features not used like expected

## Slide 5: PC Hardware: Memory
IBM PC
  16KB – 256KB, Expansion cards
  BIOS used 8KB
IBM XT
  64KB - 1MB, Expansion cards
  BIOS used 384 KB
IBM AT
  Up to 16MB, 80286 address space

## Slide 6: PC Hardware: Drives
Low Budget
  Tape drives
  Floppy drive
Floppy Drives Very Popular
IBM PC
  Up to 2 5.25” single sided floppy drives
IBM XT
  Up to 2 5.25” double sided floppy drives
  10MB hard drive
IBM AT
  Up to 2 5.25” high density floppy drives
  20MB hard drive

## Slide 7: PC Hardware: IO
Keyboard
  Very good keyboard -> popularity
Monitor
  MDA – Text mode only
  CGA – Text and graphics
  EGA – Text and higher resolution graphics
Serial and Printer Ports
  Modems
  Mice
  Printers
Expansion Cards:
  Joysticks
  Cash Drawers
  Special Machinery

## Slide 8: PC: Limitations
Memory
  Little available to programmer
    Cost and address space
  Fixed with expansion cards and 80286
Storage Capacity
  Hard drives quite expensive
  Fixed with IBM XT
Graphics:
  Limited Resolutions
Multi-Tasking & Memory Management
  8088 – No Support
  80286 – Added support, not backwards compatible -> not used

## Slide 9: The Disk Operating System
Root is CP/M
Lightweight Single-Task Single-User Program Loader
IBM asked Microsoft for OS
Microsoft sourced 86-DOS from Tim Patterson
Modified into MS-DOS
Licensed PCDOS to IBM

## Slide 10: DOS: Boot Process
POST
ROM Boot Loader [PC BIOS]
Disk Boot Loader [First Sector of disk]
Extra BIOS Code [IO.SYS]
SYSINIT code [IO.SYS]
MSDOS.SYS [DOS kernel]
CONFIG.SYS [Settings and Drivers]
COMMAND.COM [Shell]

## Slide 11: DOS: Memory Management
Lower Memory
  Kernel [MSDOS.SYS]
Middle Memory
  Shell [COMMAND.COM]
  Program
Upper Memory
  BIOS Code and Data
    Video Memory

## Slide 12: DOS: Memory Management
Free Memory - Arena Entries
  Headers chained together for searching
  Essentially Dynamic Partitioning
.COM
  Raw binary
  Max memory given at start
.EXE
  Has header telling DOS how much memory is needed
Memory Requests
  DOS functions

## Slide 13: DOS: File Management
FCB
  Legacy for CP/M programs
  No Directories
FAT
  Clusters
    Basic block of data
  File Allocation Table
    Index table for clusters
    Cluster Chaining
  Directory Tables
    Cluster #s
    Name, Attributes

## Slide 14: DOS: IO
Basic Functions – BIOS
  Keyboard, Screen, Drives
  Software Interrupts
Additional Devices – CONFIG.SYS
  Loaded at startup

## Slide 15: DOS: API
Basic functions:
  File access
  Starting another program
  Memory allocation
Similar to BIOS function calls
  Software interrupts
Very primitive compared to today:
  Limited libraries - programmers wrote their own for every program

## Slide 16: DOS: Limitations
No Multi-Tasking
  TSRs were closest functionality
One User
  Original design was simple program loader
No Security
  Files only protected by attributes
    System
    Hidden
    Read Only
Limited API
  No Common Libraries

## Slide 17: Impacts: Windows
PC
  PC is only as good as its OS
  PC grew out of DOS into Windows
  PC popularity -> Windows popularity
DOS
  Early Windows built on MS-DOS
  Early Windows were first graphic shells for DOS
  Windows 3.x & 9x loaded with DOS

## Slide 18: Impacts: FAT
DOS and Windows made FAT very popular
Floppy drives in PC
  PCs made floppy disk popular
  Removable drive implies inter-system data exchange
  FAT was the answer to data sharing
FAT now standard for camera storage
FAT used in Flash Drives and SD cards
Most OSs can read FAT drives

## Slide 19: Impacts: x86 Architecture
PC and DOS rose in popularity
  More hardware and software targeted at PC
  Intel created better processors with new features
Backward compatibility is important
  All x86 processors are backward compatible
  Consumer can always run old software on new machine
  Keeps consumers happy, thus reinforcing popularity